## Slide 1: The Monolithic 3D-IC
A Disruptor to the Semiconductor Industry

## Slide 2: Monolithic 3D Provides an Attractive Path to…
3D-CMOS: Monolithic 3D Logic Technology
3D-FPGA: Monolithic 3D Programmable Logic
3D-GateArray: Monolithic 3D Gate Array
3D-Repair: Yield recovery for high-density chips
3D-Flash: Monolithic 3D Flash Memory
3D-DRAM: Monolithic 3D DRAM
3D-RRAM: Monolithic 3D RRAM
3D-Imagers: Monolithic 3D Image Sensor
3D-MicroDisplay: Monolithic 3D Display
Monolithic 3D Integration with Ion-Cut Technology
Can be applied to many market segments
LOGIC
MEMORY
OPTO-ELECTRONICS

## Slide 3: Layer Transfer Technology (or “Ion-Cut” / “Smart-Cut”) The Technology Behind SOI
p- Si
Oxide
p- Si
Oxide
H
Top layer
Bottom layer
Oxide
Hydrogen implant
of top layer
Flip top layer and
bond to bottom layer
Oxide
p- Si
Oxide
H
Cleave using 400oC
anneal or sideways
mechanical force. CMP.
Oxide
Oxide
Similar process (bulk-to-bulk) used for manufacturing all SOI wafers today
p- Si

## Slide 4: Monolithic 3D NAND Flash
4x density of conventional NAND Flash, at similar number of litho steps (cost)

## Slide 5: Preview
Non-volatile memory companies  Are now going for monolithic 3D
MonolithIC 3DTM Inc.: Offers mono-crystal monolithic 3D solutions
Industry  Largely poly Si 3D memory (Toshiba BiCS, Samsung VG-NAND,…)
MonolithIC 3DTM Inc.:  Single crystal Si 3D memory
NuFlash
4x density improvement vs. NAND, with similar number of litho steps
NuRRAM
2x density improvement vs. NAND, with similar number of litho steps
1 million cycles, higher performance

## Slide 6: Ion-cut vs. other types of stacked Si
 | Poly Si with RTA | Selective epi Si | Ion-cut Si
Defect density | High | Low, but cracks exist. | Perfect single crystal Si.
Mobility | 100cm2/Vs |  | 650cm2/Vs
Variability | High |  | Low
Sub-threshold slope and Leakage | High |  | Low
Temperature stacked bottom layer exposed to typically | 700-800oC for crystallization | ~700oC | <400oC
Cost | Low |  | See next slide

## Slide 7: Ion-cut is Simple and Not Expensive Process
Industry sources  <$50 cost per wafer (ion cut = implant, bond, anneal).
Free market scenario  SOITEC basic patent had expired on Sept. 2012
Contents:
Hydrogen implant
Cleave with anneal

## Slide 8: 3D NAND Using Poly are The Next Generation
Toshiba BiCS
Vertical, poly Si
Samsung VG-NAND
Horizontal, poly Si
Macronix junction-free-NAND
Horizontal, poly Si
Poly Si  low mobility, high variation, large S-factor  this, coupled with charge-trap nature makes MLC 3D NAND very difficult!!!

## Slide 9: ITRS 2012 – NAND Flash Adapting Monolithic 3D

## Slide 10: Monolithic 3D NAND – Crystallized Si Base
Any horizontally oriented 3D NAND Implementation
 can be constructed with single crystal Silicon using ion-cut
Sub-400oC process, avoid complications with poly-Si

## Slide 11: NuFlash Memory Cell
Double gate single-crystal Si cell
Fully-depleted device
Two charge trap layers per cell
n+
n+
n+
CG
ONO layer 1
SiO2
CG
ONO layer 2

## Slide 12: Process Flow: Step 1 Fabricate peripheral circuits followed by silicon oxide layer
Silicon Oxide
Peripheral circuits

## Slide 13: Process Flow: Step 2 Transfer n+ Si layer atop peripheral circuit layer
Silicon Oxide
n+ Silicon
H implant
Silicon Oxide
Peripheral circuits
Silicon Oxide
Peripheral circuits
Top layer
Bottom layer
Silicon Oxide
n+ Silicon
H implant
Flip Top layer and bond to bottom layer

## Slide 14: Process Flow: Step 3 Cleave, CMP, oxide deposition
Silicon Oxide
Peripheral circuits
Silicon Oxide
n+ Silicon
Silicon Oxide

## Slide 15: Process Flow: Step 4 Form multiple Si layers
Silicon Oxide
Peripheral circuits
Silicon Oxide 06
n+ Silicon
Silicon Oxide
Silicon Oxide 06
Silicon Oxide
Silicon Oxide 06
Silicon Oxide

## Slide 16: Process Flow: Step 5 Use litho and etch to define layers
Silicon Oxide
Peripheral circuits
n+ Silicon
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon oxide
Symbols

## Slide 17: Process Flow: Step 6 Deposit gate dielectric, electrode, CMP, pattern and etch
n+ Silicon
Silicon oxide
Symbols
Gate electrode 3724
Gate dielectric
Silicon Oxide
Peripheral circuits
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
NAND string
Select gates

## Slide 18: Process Flow: Step 7 Oxide, CMP, form bit-lines, cell source regions
Silicon oxide
n+ Silicon
Gate electrode
Gate dielectric
Silicon oxide
Silicon Oxide
Peripheral circuits
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Wiring for select gates
Cell source regions
WL
Three Bit-Lines (BL) of n+ Si

## Slide 19: MonolithIC Flash vs. Conventional NAND vs. BiCS
MonolithIC Flash
4x improvement in density at similar number of litho steps
140 sq. mm die | Conventional NAND 22nm node | BiCS 32 layers @ 45nm node | NuFlash 8 layers @ 22nm node
Density | 64Gbit (MLC) | 128Gbit (SLC) 256Gbit (MLC) | 256Gbit (MLC)
Aspect ratio |  | 60:1  hard to manufacture | 16:1
Scaling |  | Difficult, only scale up | Practical, scale up and sideways
Estimates from 2010 VLSI Symposium short course on 3D Memory.

## Slide 20: Monolithic 3D DRAM
3.3x density of conventional DRAM, at similar number of litho steps (cost)

## Slide 21: Process Flow: Step 3 Cleave along H plane, then CMP
Silicon Oxide
Peripheral circuits
Silicon Oxide
p Silicon
Silicon Oxide
Peripheral circuits

## Slide 22: Process Flow: Step 4 Using a litho step, form n+ regions using implant
Silicon Oxide
Peripheral circuits
Silicon Oxide
p
n+
n+
n+
p

## Slide 23: Process Flow: Step 5 Deposit oxide layer
Silicon Oxide
Peripheral circuits
Silicon Oxide
Silicon Oxide
n+
p

## Slide 24: Process Flow: Step 6 Using methods similar to Steps 2-5, form multiple Si/SiO2 layers, RTA
Silicon Oxide
Peripheral circuits
Silicon Oxide 06
Silicon Oxide
Silicon Oxide 06
Silicon Oxide
Silicon Oxide 06
Silicon Oxide
p
n+
n+
n+
p

## Slide 25: Process Flow: Step 7 Use lithography and etch to define Silicon regions
Silicon Oxide
Peripheral circuits
p Silicon
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon oxide
Symbols
n+ Silicon
This n+ Si region will act as wiring for the array… details later

## Slide 26: Process Flow: Step 8 Deposit gate dielectric, gate electrode materials, CMP, litho and etch
Silicon Oxide
Peripheral circuits
n+ Silicon
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon oxide
Symbols
Gate electrode
Gate dielectric

## Slide 27: Process Flow: Step 9 Deposit oxide, CMP. Oxide shown transparent for clarity.
Silicon Oxide
Peripheral circuits
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon oxide
Word Line (WL)
WL current path
SL current path
Source-Line (SL)
n+ Silicon
Silicon oxide
Symbols
Gate electrode
Gate dielectric
Silicon oxide

## Slide 28: Process Flow: Step 10 Make Bit Line (BL) contacts that are shared among various layers.
Silicon Oxide
Peripheral circuits
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon oxide
WL
SL
WL current path
SL current path
BL contact
n+ Silicon
Silicon oxide
Symbols
Gate electrode
Gate dielectric
Silicon oxide
BL contact

## Slide 29: Process Flow: Step 11 Construct BLs, then contacts to BLs, WLs and SLs at edges of memory array using methods in [Tanaka, et al., VLSI 2007]
Silicon Oxide
Peripheral circuits
n+ Silicon
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon Oxide 06
Silicon oxide
Symbols
Gate electrode
Gate dielectric
Silicon oxide
WL
SL
SL current
BL contact
BL
WL current
BL current
BL

## Slide 30: Some cross-sectional views for clarity. Each floating-body cell has unique combination of BL, WL, SL

## Slide 31: Density estimation
 | Conventional stacked capacitor DRAM | Monolithic 3D DRAM with 4 memory layers
Cell size | 6F2 | Since non self-aligned, 7.2F2
Density | x | 3.3x
Number of litho steps | 26 (with 3 stacked cap. masks) | ~26 (3 extra masks for memory layers, but no stacked cap. masks)
3.3x improvement in density vs. standard DRAM, but similar number of critical litho steps!!!
Negligible prior work in monolithic 3D DRAM with shared litho steps, poly Si 3D doesn’t work for DRAM (unlike NAND flash) due to leakage

## Slide 32: Scalability
MonolithIC 3D Inc. Patents Pending
32

## Slide 33: Scalability
Multiple generations of cost per bit improvement possible
(e.g.) 22nm 2D 
22nm 3D 2 layers 
22nm 3D 4 layers  ...
Use same 22nm litho tools for 6+ years above. Tool value goes down 50% every 2 years  Cheap 
Avoids cost + risk of next-gen litho
MonolithIC 3D Inc. Patents Pending
33

## Slide 34: Avoids the difficulties with scaling-down
EUV delays and risk
MonolithIC 3D Inc. Patents Pending
34
(EETimes 2002)
"EUV to be in production in 2007"
(EETimes 2003)
"EUV to be leading candidate for the 32nm in 2009"
(EETimes 2004)
"EUV to be pushed out to 2013"
(EETimes 2010)
"EUV late for 10nm node milestone in 2015"
Capacitor manufacturing
 | 45 nm | 32 nm | 22 nm | 15 nm | 10 nm
ε | 40 | 50 | 60 | 65 | 70
AR | 47 | 56 | 99 | 147 | 193
Continuous transistor updates
Planar  RCAT  S-RCAT  Finfet
 Vertical devices

## Slide 35: Summary of Monolithic 3D DRAM Technology
3.3x density of conventional DRAM, at similar number of litho steps (cost)
Scalable (e.g.) 22nm 2D  22nm 3D 2 layers  22nm 3D 4 layers  ...
Cheap depreciated tools, less litho cost + risk
Avoids cap. & transistor upgrades challenges
MonolithIC 3D Inc. Patents Pending
35
Monolithic 3D with shared litho steps
Single crystal Si
Floating body RAM
Under development...

## Slide 36
MonolithIC 3D Inc. Patents Pending
36
Monolithic 3D R-RAM
2x density improvement vs. conventional NAND
1M cycles endurance, low latency, high performance

## Slide 37: R-RAM: A Promising Next Generation Memory
Below data from IEDM 2009 for a (transistor + R-RAM )  Promising
Well-known and simple materials (unlike PCM), low switching power, good endurance.
TiN
HfOx
Ti
TiN
AlCu

## Slide 38: Potential Architectures for Integrating RRAM into Arrays: (1) Poly Si diode Selectors
Matrix [ISSCC 2003]
Hitachi [VLSI 2009]
p
n
RRAM
Unidirectional current flow  bad for bipolar RRAM
Poly very leaky, low drive current vs. single crystal Si
 bandwidth/power good for storage apps?
Diode RTA  W wiring, not Cu or Al.

## Slide 39: Potential Architectures for Integrating RRAM into Arrays: (2) Transistor Selectors at Bottom
Leakage of unselected cells in array
BW/power/die size not good enough for storage
Samsung: [VLSI 2009]

## Slide 40: Key Characteristics of MonolithIC R-RAM
Single crystal Si Transistor Selectors  Several orders of magnitude lower leakage  Competitive or much better BW/power vs. NAND
Bipolar Selector
Cu or Al wiring
Scalable architecture, with several generations cost per bit improvement
Low number of litho steps, number of litho steps competes with NAND (4 critical steps)

## Slide 41: Process Flow
This architecture:
1T-1R
Double gated depletion-mode transistors
While described for RRAM here, could also be done for PCM and other rewritable memory materials with easy adaptation

## Slide 42
MonolithIC 3D Inc. Patents Pending
42
Monolithic 3D IC technology is applied to producing a monolithically stacked single crystal silicon transistor selected RRAM or PCM memory. 1T-1R memory cells enjoy a low number of (shared) litho steps, Cu or Al wiring, and a scalable architecture. An efficient bipolar RRAM is now possible. Peripheral circuits below the monolithic memory stack deliver control functions.
Reduce bit cost of resistive memories without investing in expensive scaling down.
Technology

## Slide 43: Monolithic 3D Resistive Memories
MonolithIC 3D Inc. Patents Pending
43

## Slide 44
MonolithIC 3D Inc. Patents Pending
44
Benefits
2-3X the density of NAND flash with similar number of litho steps
Single crystal silicon bidirectional transistor selector
Shared litho steps among many memory layers
All layer single crystal silicon provides negligible leakage & dramatically better performance/power
Scalable: Multiple generations of cost-per-bit improvement for same equipment cost and process node: use the same fab for 3 generations
Forestalls next gen litho-tool risk
Density & non-volatility of Flash, but speeds and endurance approaching DRAM
Benefits

## Slide 45: Process Flow

## Slide 46
MonolithIC 3D Inc. Patents Pending
46
Our 3D resistive memory technology provides:
Shared litho steps to create stacked memory at low cost
Compatible with whatever resistive material you choose
Single crystal Si junctionless transistor selectors allow bipolar operation
Process Flow

## Slide 47
MonolithIC 3D Inc. Patents Pending
47
Step 1: Ion-cut is used to transfer a n+ single crystal silicon layer atop the peripheral circuits of the resistive memory as depicted in Fig. 8. Notice how the peripheral circuits are placed under the memory array... this improves the array efficiency and allows smaller-size blocks that offer high performance. Also, the n+ dopants are pre-activated before layer transfer.
Step 2: Using steps similar to Step 1, a silicon-silicon dioxide multilayer sandwich is formed as described in Fig. 9.
Step 3: Using the same litho and etch step, multiple layers of memory are defined as shown in Fig. 10.
Step 4: Gates are formed for multiple levels of memory at the same time as described in Fig. 11.
The steps involved in constructing our 3D resistive memory are as follows:

## Slide 48
MonolithIC 3D Inc. Patents Pending
48
Step 5: Using another shared litho step, a via hole is made to multiple levels of memory. A resistive memory element (such as titanium oxide) is deposited following which an electrode is deposited and CMPed (Fig. 12). WL, SL and BL are acronyms for Word Line, Source Line and Bit Line respectively.
Step 6: Bit-lines are then made. Contacts to multiple levels of memory are defined with shared litho steps using a process described in [Tanaka, et al., Symposium on VLSI Technology, 2007]. Fig. 13 and Fig. 14 reveal the structure after this step. Notice how each memory cell consists of a junctionless transistor in series with a RW memory device. Using carefully chosen biases to bit-lines (BLs), word-lines (WLs) and source-lines (SLs), each bit in the memory array can be uniquely addressed.
The steps involved in constructing our 3D resistive memory are as follows:

## Slide 49: Process Flow
MonolithIC 3D Inc. Patents Pending
49

## Slide 50: Process Flow
MonolithIC 3D Inc. Patents Pending
50

## Slide 51: Process Flow
MonolithIC 3D Inc. Patents Pending
51

## Slide 52: Process Flow
MonolithIC 3D Inc. Patents Pending
52

## Slide 53: Process Flow
MonolithIC 3D Inc. Patents Pending
53

## Slide 54: Process Flow
MonolithIC 3D Inc. Patents Pending
54

## Slide 55: Process Flow
MonolithIC 3D Inc. Patents Pending
55

## Slide 56: Array Bias Schemes
Selected cell: Drive current > 40uA as long as voltage drop across select transistor > 1.3V
Un-selected and half-selected cells: Leakage negligible. Huge array sizes possible
Top layer of 3D memory
Bottom layer of 3D memory
4V
1V
2.5V
2.5V
2.5V
2.5V
2.5V
2.5V
3.5V
3.5V
0V
0V
0V
0V
0V
0V
1.5V
1.5V
0V
0V
0V
0V
0V
0V
3.5V
3.5V
3.5V
1.5V
4V
1.5V
BL
SL

## Slide 57: Approximate Density Estimations
 | NAND | Poly Diode Selected RRAM | NuRRAM
Cell size | 4F2 | 4F2 | 18F2
Bits per cell | 2 | 1 | 2
Number of memory levels | 1 | 8 | 10 for 26:1 aspect ratio
Critical Litho steps per level of memory | 4 | ~2 per level | ~5 for 10 levels
Effective density @ 15nm node (memory only) | 2F2 and 4 critical litho steps | 0.5F2 and 16 critical litho steps | 0.9F2 and 5 critical litho steps
MonolithIC RRAM reduces cell size keeping number of litho steps low.
Possible in poly Si also

## Slide 58: Comparison of poly diode selected R-RAM and MonolithIC R-RAM
 | Poly Diode Selected RRAM | MonolithIC 3D R-RAM
Effective density | 0.5F2 and 16 litho steps | 0.9F2 and 5 litho steps
Selector | Two-terminal poly device | Three-terminal single crystal device
Leakage in array | High | Negligible
Bipolar operation possible? | No, pin diode is unidirectional | Yes, transistor selector
Forward current drive | Low | High

## Slide 59: Array Specs
A high-density NVM with excellent bandwidth, low power consumption, high-endurance and fast random access times!
Cell size = 9F x 2F/ (10 layers) x (2 bits per cell) ~ 0.9F2
Access time < 5ns for memory element, random access possible
Endurance > 1M cycles
Leakage of unselected cells negligible  bandwidth and power consumption numbers could be much better than NAND flash memory

## Slide 60: Summary of MonolithIC R-RAM
Novel 3D resistive memory architecture.
Single crystal Si or poly Si, applicable to many RW materials.
Three-terminal select device (transistor).
0.9F2 cell, but just 5 critical litho steps.
  2x density improvement vs. conventional NAND.
  Low number of litho steps vs. today’s 3D RW memories a key advantage.
1M cycles endurance, low latency, high performance due to transistor selector and lack of leakage
 A Storage-Class Memory solution

## Slide 61
MonolithIC 3D Inc. Patents Pending
61
© Copyright MonolithIC 3D Inc. , the Next-Generation 3D-IC Company, 2013 - All Rights Reserved, Patents Pending